## Slide 1: Hacking of Wireless Communication
A Presentation by Tyler Gwiazdowski, Ellie Deskins, Taylor Waldo,
Bennet Marsee, Dimitri Montgomery, and Landen Ramsey
05/06/25

## Slide 2: Wireless Security Basics
Secures data sent over wireless networks
Encryption scrambles data; only authorized users can decrypt it
WEP, WPA, WPA2, and WPA3 are Wi-Fi encryption protocols
Used in routers to protect data between devices and access points

## Slide 3: WEP (Wired Equivalent Privacy)
Introduced in 1990s to secure data between clients and access points
Uses RC4 stream cipher for encryption & authentication
Originally used a 40-bit key, later upgrade to 104-bit
Weak IV & flawed authentication made WEP insecure
Eventually replaced due to serious vulnerabilities

## Slide 4: WPA (Wi-Fi Protected Access)
Released in 2003 as a quick fix to WEP flaws
Stopgap by Wi-Fi Alliance while IEEE developed WPA2
Two modes:
Enterprise (802.1X + authentication server)
Personal (Pre-Shared Key)
Still based on RC4 encryption
Introduced TKIP for stronger security, including:
256-bit keys
Per-packet key mixing
Auto key updates
Message Integrity Check (MIC)
48-bit initialization vector
Improved protection against key reuse and replay attacks

## Slide 5: WPA2
Introduced in 2004 as the IEEE 802.11i standard
Offers Personal and Enterprise modes like WPA
Replaces RC4/TKIP with AES and CCMP for stronger encryption
AES: U.S. gov-developed; uses 128, 192, or 256-bit symmetric keys
CCMP: Ensures confidentiality and data integrity
Supports fast roaming between access points without reauthentication
Uses a 4-way handshake to establish secure connections
Vulnerable to KRACK attack (Key Reinstallation Attack)
WPA3 fixes KRACK by enforcing stronger handshake validation

## Slide 6: Cracking Methods WEP
WEP Overview (brief):
Uses RC4 encryption with a 24-bit Initialization Vector (IV).
Vulnerable due to IV reuse, no replay protection, and static keys.
Cracking Methods:
Passive IV Collection:
  Attackers listen to network traffic to collect IVs.
  Tools like airodump-ng get enough packets to break the key.
ARP Replay Attack:
  Forces the router to generate more traffic by injecting fake ARP requests.
  Speeds up IV collection.
Fragmentation Attack:
  Exploits packet fragments to inject packets and reconstruct the key.
Chop-Chop Attack:
  Decrypts packets byte-by-byte by modifying and reinjecting them, even without knowing the key.
  Time to Crack:
Can be broken in minutes once enough packets (10K–100K) are collected.

## Slide 7: Cracking Methods WPA
WPA Overview:
Uses TKIP + RC4, improves key rotation and adds MIC for integrity.
Relies on 4-way handshake to establish session keys.
Cracking Methods:
Handshake Capture + Dictionary Attack:
  Sniff the 4-way handshake using tools like airodump-ng.
  Crack offline with wordlists (Crack password using wordlist rockyou.txt which is in video)
Evil Twin Attack (WPA-Phishing):
  Clone a network with tools like Fluxion.
  Disconnect clients and collect passwords when they reconnect to the rogue AP.
Downgrade Attacks:
  Exploit routers that go back to WPA from WPA2, reintroducing TKIP vulnerabilities
Effectiveness:
Success depends entirely on password strength and user behavior (social engineering).

## Slide 8
Cracking Methods
WPA2
Evil Twin + Captive Portal (Fluxion):
  Fake AP mimics real network and requests passphrase through a phishing web page.
Krack Attack (Academic - Key Reinstallation):
  Exploits flaws in the 4-way handshake to decrypt traffic (patchable, but noteworthy).
WPA2 Overview (brief):
Uses AES-CCMP, considered secure in protocol design.
Most attacks target WPA2-PSK with poor passwords.
Cracking Methods:
4-Way Handshake Attack – Dictionary Attack:
  Similar to WPA, capture handshake and run brute-force/dictionary attacks.
  Use GPU-powered tools like hashcat for faster cracking.(Crack password using wordlist rockyou.txt which is in video)
PMKID Attack (Clientless):
  Some routers broadcast PMKID (a hash of the passphrase) even without client interaction.
  Captured using hcxdumptool → converted with hcxpcapngtool → cracked with hashcat.
Effectiveness:
Much harder to crack than WEP or WPA unless weak PSKs or misconfigured routers are used.

## Slide 9: Key reinstallation Attack (KRANK) Vulnerability of WPA2:
Connection begins with a four way handshake between endpoint and access point in which they acknowledge they know an authentication code.
Access point then passes a encryption key to the client.
If an endpoint does not acknowledge the key has been received, it is re sent and re installed repeatedly
Therefore, attackers have the chance to intercept the message, determine the key and crack the encryption protocol.

## Slide 10: WPA3
Launched in 2018 by the Wi-Fi Alliance
Successor to WPA2 with Personal and Enterprise modes
Requires Protected Management Frames (PMF)
Standardizes 128-bit encryption (192-bit optional for Enterprise)
Uses AES-128 + CCMP-128 (Personal mode)
Replaces 4-way handshake with SAE
  One-time credentials, no key reuse
  Resists KRACK and brute force attacks

## Slide 11: WPA3 Simultaneous Authentication of Equals System
Either client or access point can initiate contact
Each device transmits their authentication credentials in a discrete one time message as opposed to multiple re sends
SAE eliminates the use of encryption keys and requires a new authentication passphrase for every interaction.
Protects confidentiality, and the possibility of the decryption key being deciphered.
SAE also mandates active on site authentication attempts and flags anyone who exceeds a limit of login attempts, helping prevent brute force attacks.

## Slide 12
🔐 Wi-Fi Security Protocol Comparison Table
Feature | WEP | WPA | WPA2 | WPA3
Released | 1997 | 2003 | 2004 | 2018
Encryption | RC4 with static key | TKIP (RC4-based) | AES | AES
Authentication | Shared Key / Open System | PSK / 802.1X | PSK / 802.1X | SAE (Personal) / 802.1X (Enterprise)
Security Level | Very weak | Moderate (outdated) | Strong (if patched) | Very Strong (modern)
Vulnerabilities | Easy to crack in minutes | TKIP flaws | KRACK (if unpatched) | Early bugs (patched); strong overall
Notable Additions | Basic encryption | MIC, dynamic keys | AES, CCMP | SAE, OWE, PMF, Forward Secrecy
Status Today | Deprecated & insecure | Obsolete | Still widely used | Modern standard

## Slide 13: Ways to Develop Existing Wi-Fi Security Methods
Transition to Post-Quantum Cryptography (PQC)
Enhance Key Management
Add Machine Learning to Threat Detection
Tighten IoT Device Security
Better User Onboarding & Certificate Use
Multi-Factor Authentication (MFA) for Wi-Fi
Frequent Key Rotation
Privacy Enhancements

## Slide 14: Video
https://youtu.be/-cY53krsz2U?si=AIyCd_swDI4j_r2V

## Slide 15
Works Cited:
Irei, Alissa. “Wireless Security: WEP, WPA, WPA2 and WPA3 Differences.” TechTarget, TechTarget, 6 Dec. 2022, www.techtarget.com/searchnetworking/feature/Wireless-encryption-basics-Understanding-WEP-WPA-and-WPA2.
Vanhoef, Mathy. “KRACK Attacks: Breaking WPA2.” Krackattacks.com, 2017, www.krackattacks.com/.
“Aircrack-Ng - Main Documentation.” Www.aircrack-Ng.org, www.aircrack-ng.org/documentation.html.
“Aircrack-Ng - Main Documentation.” Www.aircrack-Ng.org, www.aircrack-ng.org/documentation.html.